## Slide 1: 19PHY113-
Computational Engineering
Mechanics 2

## Slide 2: TEAM MEMBERS - 05
DIVITH PHOGAT : (CB.EN.U4AIE20013)
JAYANTH M: (CB.EN.U4AIE20024)
KARNATI SAI PRASHANTH : (CB.EN.U4AIE20027)
P. Vishnu Reddy: (CB.EN.U4AIE20048)

## Slide 3: Table of Contents 1 3 4 2
Mechanism And Its Types
INTRODUCTION
FOURBAR MECHANISM
APPLICATION

## Slide 4: INTRODUCTION
If a number of bodies assembled in such a way that the motion of one body causes constrained and predictable motion to other bodies, then it is called mechanism. On another side, a machine is a mechanism or a combination of the mechanism. In addition to imparting motion to other parts, the machine also converts available mechanical energy into desired work

## Slide 5: OBJECTIVE OF THE WORK:
We will be focusing on cutting the shortcomings in this mechanism.
Most important is that we are not aware of the fact that how efficiently we can use this mechanism like:
Robert's mechanism can easily be used for civil and military purposes but there also it is needed to be little cost effective and fast.
This mechanism can also be used in plantation (for digging the earth if we attach) plus for harvesting as well.
One more thing, whenever we visit the library, we must spend at least an hour to find a specific book. Why not rack of books of specific title or category are placed at point p1 and a button is connected to that point. Whenever user push that button, the whole rack is Infront of him.

## Slide 6: Robert's mechanism Synthesis
The Englishman Roberts had proposed an approximate solution, based on a three-rod mechanism and on a CPD blade in the shape of an isosceles triangle.
This is a four bar mechanism, where, CPD is a single integral link.
Also, dimensions AC BD, CP and PD are all equal and
AD = 2 AP
Point P of the mechanism moves very nearly along line AD.

## Slide 7: Designing Optimum Straight-Line Fourbar Linkages
Given the fact that an exact straight line can be generated with six or more links using only revolute joints, why use a fourbar approximate straight-line linkage at all?
One reason is the desire for simplicity in machine design. The pin-jointed fourbar is the simplest possible one-DOF mechanism.
Another reason is that a very good approximation to a true straight line can be obtained with just four links, and this is often "good enough" for the needs of the machine being designed.
Manufacturing tolerances will, after all, cause any mechanism's performance to be less than ideal. As the number of links and joints increases, the probability that an exact-straight-line mechanism will deliver its theoretical performance in practice is obviously reduced

## Slide 8: STRAIGHT LINE MECHANISMS
One of the most common forms of the constraint mechanisms is that it permits only relative motion of an oscillatory nature along a straight line. The mechanisms used for this purpose are called straight line mechanisms.
These mechanisms are of the following two types:
  1. in which only turning pairs are used, and
  2. in which one sliding pair is used.
These two types of mechanisms may produce exact straight-line motion or approximate straight-line motion

## Slide 9: Condition for Exact Straight Line Motion Mechanisms
The principle adopted for a mathematically correct or
exact straight line motion is described in Fig.
Let O be a point on the circumference of a circle of diameter OP. Let OA be any chord and B is a point on OA produced, such that
OA x 0B = constant
Then the locus of a point B will be a straight line
perpendicular to the diameter OP.

## Slide 10: ROBERT’S LINKAGE:
Roberts Linkage is a mechanism of triple rocker kind in which none of the links rotate through 360°.
If suppose OA=BC=a, OC=2h, AB=AP=BP=h and a=h= 1 (inch)
Click to add text

## Slide 11: SMALLEST ANGLE:
From the limiting positions illustrated above , by cosine law,
L32 = L02 + (L1 + L2)2 - 2 L0 (L1 + L2) cos θmin
=> θmin = cos-1 {[ L02 + (L1 + L2)2 - L32] / 2 L0 (L1 + L2)}
θmin = cos^-1{[(2h)^2+(a+h)^2-(a)^2]/2(2h)(a+h)}
θmin = cos^-1{[4h^2+(a+h)^2-a^2]/(4h)(a+h)
θmin = cos^-1{[4+(2)^2-(1)^2]/4(2)}
θmin = cos^-1{[4+4-1]/8}
θmin = cos^-1{[⅞]}
θmin = 28.95 deg

## Slide 12: LARGEST ANGLE:
Calculating for the largest angle:
(L2+ L3)2 = L02 + L12 - 2 L0.L1 cos θmax
θmax = cos-1 {[ L02 + L12 - (L2 + L3)2]/ 2 L0.L1 }
θmax = cos-1 {[ (2h)^2+(a)^2-(h+a)^2]/2(2h)(a)
θmax = cos-1 {[ 4h^2+a^2-(h+a)^2]/2(2h)(a)
θmax = cos-1 {[ 4+1-(2)^2]/(2)(2)
θmax = cos-1 {[ 4+1-4]/4}
θmax = cos-1 {[¼]}
θmax = 75 deg 52 rad

## Slide 13: POSITION OF MOVING POINT:
The vector representation of a symmetrical Roberts Linkage is
shown In the below figure
The coordinates (x1,y1) and (x2,y2) are calculated as follows,
X1 = r1 cos Φ
Y1 = r1 sin Φ
X2= X1+r2X
Y2= Y1+r2Y

## Slide 14: ROBERT’S MECHANISM IN GEOGEBRA:
GeoGebra is dynamic mathematics software for all levels of education that brings together geometry, algebra, spreadsheets, graphing, statistics, and calculus in one easy-to-use package. GeoGebra is a rapidly expanding community of millions of users located in about every country. GeoGebra has become the leading provider of dynamic mathematics software, supporting science, technology, engineering, and mathematics (STEM) education and innovations in teaching, and learning worldwide.
We have Done the Animation of the Roberts Mechanism in GeoGebra:
Lengths:
AB = CD= 7 units
BP = CP = 6.32units
BC = 3 units
AD = 10 units
Maximum Angle = 69.5 deg
Minimum Angle = 40 deg

## Slide 15: APPLICATIONS

## Slide 16: Thank You